## Slide 1: SCA: A Secure CNN Accelerator for Both Training and Inference
Lei Zhao, Youtao Zhang, Jun Yang
University of Pittsburgh

## Slide 2: About ME
My name is Lei Zhao.
PhD candidate in the University of Pittsburgh.
Research areas:
Computer architecture.
Domain specific accelerator design.
Secure and privacy-preserving machine learning.

## Slide 3: Neural Networks are widely used in mobile devices
Navigation
Translation
Health care
Facial recognition
Speech recognition
…

## Slide 4: Models need to be protected
Extract the model
Retrain with custom data on device
Encryption
CPU
Memory
Storage
Decryption
Encryption

## Slide 5
Motivation
Background
Design
Methodology
Results
Conclusion
Use stochastic computing for cheaper computation
Use SC precision loss as hardware fingerprint for protection
Wb
Weights are stored in binary
format off-chip
0.12, 0.44 …, -0.5
… … … …
0.55, -0.44 …, 1.34
Low accuracy if used in CNN prediction
Weights are stored in SC
format on-chip
0.11, 0.47 …, -0.48
… … … …
0.57, -0.42 …, 1.35
Wsc
Can produce accuracy prediction
0.58
0.65

## Slide 6
Background
Stochastic Computing
Design
Methodology
Results
Conclusion
SC Numbers are represented by the probability of 1s in a bit stream
E.g., : X = 0.75 = 0.110b = 1001111011011111sc
Binary format
SC format
MUX
Asc
Bsc
Csc
0.5
Asc
Bsc
Csc
XNOR
Addition
Multiplication
Use simple logic to implement addition and multiplication

## Slide 7
eDRAM
Background
Design
Methodology
Results
Conclusion
abstract
Need refresh operation to restore value
‘0’ bit
‘1’ bit
refresh
Leak charge
Cell structure

## Slide 8
SC based Protection
Generating device dependent bit streams
❶ Fully charge a row of cells
❷ Reduce refresh frequency
❹ Conversion
Background
Design
Methodology
Results
Conclusion
…
❸ Read out
P(X=1)≈0.5
1 0 0 1 0 1 0
P(X=1)<0.5
P(X=1)>0.5
00…0
11…1
Victim row

## Slide 9
SC based Protection
Embedding device dependent information into NN models
Background
Design
Methodology
Results
Conclusion
Convert weights from
binary to SC format:
Wb Wsc
Forward propagate
using Wsc to get Loss
Calculate derivative of Loss
over binary weights:
Update the binary weights:
Wb = Wb-η
Neural networks are over-parameterized

## Slide 10
SC based Protection
Background
Design
Methodology
Results
Conclusion
 | Target Device | Pirate Device | No SC
MNIST-MLPS | 99.73% | 57.98% | 60.25%
MNIST-MLPM | 99.69% | 21.57% | 24.75%
MNIST-MLPL | 99.99% | 22.99% | 26.38%
MNIST-CNN | 99.07% | 14.27% | 81.82%
SVHN-CNN | 99.84% | 69.04% | 60.9%
Cifar10-CNN | 99.99% | 41.86% | 53.44%
The weights are training using device A’s memory to generate SC numbers
  Target Device: Test using device A’s memory to generate SC numbers
  Pirate Device: Test using another device B’s memory to generate SC numbers
  No SC: Test using binary numbers directly

## Slide 11
Secure Learning Phase
Background
Design
Methodology
Results
Conclusion
CNNs are capable to learn the difference between Wb and Wsc.
Distance = (Wb – Wsc)2
Change the offset to insert 1s and 0s.
Each epoch only changes one layer’s offset.
00…0
00…0
00…0
Epoch 1
Epoch 2
Epoch 3
Solution

## Slide 12
Secure Learning Phase
Background
Design
Methodology
Results
Conclusion
Chart: MNIST-MLPS
Chart: MNIST-MLPM
Chart: MNIST-MLPM
Chart: MNIST-CNN
Chart: MNIST-CNN
Chart: Cifar10-CNN
Distance stops decreasing when training converges

## Slide 13
Optimized MAC Operation
1
1
0
0
1
0
1
0
1
1
0
1
MUX based adder
APC based adder
Background
Design
Methodology
Results
Conclusion
APC
APC
APC
APC
…
Group adder
+
+
+
…
…
Adder tree
1
1
1
0
0
0
1
1
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
XNOR
256
256
256
MUX
Simple logic
Multiple cycles
Low precision
High precision
More gates
Needs adders for subsequent operations
MUX
MUX
MUX
MUX
Concat
Concat
Concat
Concat
64
64
256

## Slide 14
Accelerator Overview
Background
Design
Methodology
Results
Conclusion
Off-chip
Mem
Controller
Weight Buffer
Input Buffer
Output Buffer
SCC Unit
Local Weights
Local Inputs
Local Outputs
MAC Unit
Activation
Pool
Wb
Inb
Outb
Wb
Inb
Wsc
Insc
Wsc
Insc
+
Outb
Outb
Outb
DRAM
eRAM
SRAM
Whenever data are stored in off-chip memory, they are in binary format, thus being protected

## Slide 15
Background
Design
Methodology
Results
Conclusion
Accelerator characteristics
CNN framework
Custom CNN frame written in C++ with CUDA acceleration
Replace all computations in C++ and CUDA kernels with SC bit-wise operations
Benchmarks
Schemes
AEP [ICCAD`2017] | Use dram soft error on binary format weights to protect CNN models
SC-CNN [DAC`2017] | SC accelerated CNN accelerator design
SCA-1 | SC based protection on CNN models
SCA-2 | SCA-1 with optimized MAC operation
MNIST-MLPS | 250-10
MNIST-MLPM | 500-250-10
MNIST-MLPL | 1000-500-250-10
MNIST-CNN | conv5x20-pool2-500-10
SVHN-CNN | conv5x32-pool2-conv5x64-pool2-256-10
Cifar10-CNN | conv4x32-pool2-conv5x32-pool2-conv5x64-pool-500-10

## Slide 16
Performance
Chart: Speedup
| MNIST-MLPS | MNIST-MLPM | MNIST-MLPL | MNIST-CNN | SVHN-CNN | Cifar10-CNN | Average
AEP | 1 | 1 | 1 | 1 | 1 | 1 | 1
SC-CNN | 7.5812 | 7.5166 | 7.4956 | 2.2847 | 5.1348 | 12.9096 | 7.1538
SCA-1 | 8.3097 | 13.3629 | 13.3256 | 4.0513 | 9.0375 | 22.5474 | 11.7724
SCA-2 | 31.8057 | 39.9716 | 39.8773 | 11.851 | 24.7072 | 57.1511 | 34.2273
Background
Design
Methodology
Results
Conclusion
4.8X
Normalized to APE.
SCA-1 achieves 11.7X speedup by using memory read based SC conversion.
SCA-2 further improves performance to 34.2X due to optimized MAC and shorter bit streams.

## Slide 17
Energy
Chart: Normalized Energy
| MNIST-MLPS | MNIST-MLPM | MNIST-MLPL | MNIST-CNN | SVHN-CNN | Cifar10-CNN | Average
SC-CNN | 0.04401 | 0.11437 | 0.30485 | 0.12196 | 0.03812 | 0.00785 | 0.10519
SCA-1 | 0.03964 | 0.05776 | 0.15395 | 0.06179 | 0.01949 | 0.00406 | 0.05611
SCA-2 | 0.00998 | 0.01493 | 0.03977 | 0.01652 | 0.00576 | 0.00133 | 0.01472
Background
Design
Methodology
Results
Conclusion
Normalized to APE.
SCA-1 consumes 94.4% less energy than SC-CNN by using DRAM read based SC conversion.
SCA-2 further reduces 98.6% energy compared to AEP.

## Slide 18
Background
Design
Methodology
Results
Conclusion
Motivation
Mobile devices have a requirement for protection and fast computation.
Solution
Use SC for fast computation.
Use precision loss during SC conversion as hardware fingerprint.
Also support on device training.
Results
Prevents model to run (both training and inference) on unauthorized device.
Achieves 34.2X speedup.
Saves 98.6% energy.

## Slide 19: Thanks for watching Questions