## Slide 1
AEP: An Error–bearing Neural Network Accelerator for Energy Efficiency and Model Protection
Lei Zhao+, Youtao Zhang+, Jun Yang*
+Computer Science Department, University of Pittsburgh
*Electrical and Computer Engineering Department, University of Pittsburgh

## Slide 2: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 3: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 4: Neural Networks In Applications
Neural Networks
Military
Self driving cars
Augmented reality
Games
Security

## Slide 5: Neural Networks Need To Be Protected
TRAINING DATA PRIVACY
COMPUTATION POWER
TRAINING TIME
TRANSFER LEARNING
INTELLECTUAL PROPERTY
Patient privacy
Commercial data
Super computers
Cloud computing
Takes weeks to
months of training
Pretrained models
can be reused for
other related tasks

## Slide 6: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 7: Observation
0
1
1
0
0
1
…
Iter 0
0
0
1
1
1
1
…
Iter 1
0
1
1
1
0
1
1
0
0
…
Iter 2
0
0
1
0
0
1
0
1
1
…
Iter 3
0
0
1
1
Gradient methods find the local minima in the error surface of deep models
The solution is not unique
multiple solutions

## Slide 8: Observation
0
1
1
0
0
1
…
Iter 0
0
1
1
1
0
1
…
Iter 1
1
0
1
1
1
0
0
0
1
…
Iter 3
1
0
0
1
1
1
0
1
0
0
…
Iter 2
0
1
0
1
0
The learning procedure adapts to the error automatically
The errors force the learning to find other solutions (local minima)

## Slide 9: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 10: Overview
Server
Mask Database
①
②
③
Target Device
Pirate Device
weights
weights
Extract error masks from target device, and store them into Mask Database
Train the NN with error masks on server
The trained weights can only work on the target device
Even if the weights are stolen and deployed on the pirate device, they are useless
How to generate
device dependent
error masks
How to integrate
error masks into
trained weights
How secure it is

## Slide 11: Outline
Background
Observation
Design Overview
Design Details
  Error Masks
  Error-bearing Training
  Securing Error Masks at Client Side
Experiment Setup
Results

## Slide 12: Generating Error Masks
cell
bitline
precharged
charge
sharing
sense
amplification
restored
precharged
cell
cell
cell
cell
tRCD
tRAS
tRP
bitline
bitline
bitline
bitline
tRCD: time to read data out
tRAS: time to restore data back into cell
tRP: time to precharge bitline for next read

## Slide 13: Error Masks
M0
M1
Cells stuck-at-0
Cells stuck-at-1
M0: Mask of stuck-at-0 cells
M1: Mask of stuck-at-1 cells
The whole memory space
Post-fabrication test to extract
M0 and M1

## Slide 14: Outline
Background
Observation
Design Overview
Design Details
  Error Masks
  Error-bearing Training
  Securing Error Masks at Client Side
Experiment Setup
Results

## Slide 15: Conventional Training
N4
Loss(T, N4)
N1
W2
N2
W3
N3
W4
I
W1

## Slide 16: Error-bearing Training
I
F(W1)
F(W2)
F(W3)
F(W4)
N1
N2
N3
N4
Loss(T, N4)
W1
W2
W3
W4
F(W) = W & M0 | M1
Apply batch normalization
after each convolution and
fully connected layer

## Slide 17: Batch Normalization
When the error bits occurs in higher significant bits (integer bits), the resulted error may impact too much
Batch normalization ( ) forces the activations to have zero mean and unit variance
All parameters in batch normalization is fixed during inference, small computation overhead
y

## Slide 18: Neural Network Protection
W:
0
0
1
0
1
1
…
M0:
1
1
1
1
0
1
…
M1:
0
1
0
0
0
0
…
F(W):
0
1
1
0
0
1
…
Server
Target
M0:
1
1
1
1
0
1
…
M1:
0
1
0
0
0
0
…
W
W
F(W) = W & M0 | M1
Pirate
M’0:
1
1
0
1
1
1
…
M’1:
1
0
0
0
0
0
…
F’(W) = W & M’0 | M’1
Only F(W) can produce
satisfactory predictions

## Slide 19: Outline
Background
Observation
Design Overview
Design Details
  Error Masks
  Error-bearing Training
  Securing Error Masks at Client Side
Experiment Setup
Results

## Slide 20: Securing Error Mask At Client Side
Disable the read path of DRAM before release to user
Dynamic error mask selection
  Small area overhead (mask 4 bits, group table 6 Bytes)
  Since memory access pattern is determined for NN, the lookup is not on critical path
tRAS – 1ns
tRAS – 0ns
tRAS – 2ns
tRAS – 2ns

## Slide 21: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 22: Experiment Setup
We use Theano to explore error tolerance of different NNs
We developed a simulator based on DianNao accelerator for performance evaluation
We use 16-bit fixed point (1 sign bit, 1 integer bit, 14 fraction bits)
Schemes:
  Baseline: DianNao accelerator design, use conservative DRAM timing parameters
  AL: Adaptive Latency DRAM, reduce DRAM timing parameters but no errors
  AEP: our design, reduce tRAS aggressively to introduce errors in weights
Benchmarks:

## Slide 23: Outline
Background
Observation
Design Overview
Design Details
Experiment Setup
Results

## Slide 24: Error Tolerance
Different network has different error tolerance
  We set the threshold to 1% accuracy loss (0.1% - 5% error rate)
Some applications do always prefer very high accuracy
  Trade off between response time, energy and accuracy

## Slide 25: IP Protection Effectiveness
 | Target Device | Pirate Device | Error-Free Device
MLPS | 99.77% | 39.35% | 81.5%
MLPM | 99.38% | 28.31% | 71.43%
MLPL | 99.02% | 10.41% | 24.53%
CNN1 | 99.16% | 10.15% | 21.66%
CNN2 | 99.71% | 89.94% | 97.6%
CNN3 | 100% | 60.95% | 97.77%
Target Device: Do inference on the target device with the same error mask as used in training
Pirate Device: Do inference on a pirate device with a difference error mask as used in training
Error-Free Device: Do inference on a device without introducing errors

## Slide 26: Performance
The large improvement comes from the aggressively reduced tRAS in DRAM read.
  NNs exhibit extreme memory access intensity
72% improvement over Baseline, 32% improvement over AL

## Slide 27: Energy
AL reduces tRCD, tRAS, tWR and tRP, saves 24% energy over Baseline
Although AEP only reduces tRAS (more aggressively than AL), inference requires more reads than writes, energy save is larger (44% over Baseline)

## Slide 28: Robustness
VRT (Variable Retention Time) and chip voltage fluctuation can cause variations in error masks
VRT variation is in the order of 10-6
NNs can tolerate 1% to 15% difference in error mask

## Slide 29: Training Time
Problem
  Each device needs to be trained separately due to their unique error masks
Solution
  First train the NN without error mask to get Wno-error
  Continue training on top of Wno-error with each device’s dependent error mask applied separately

## Slide 30: Conclusion
Problem addressed
  Protect Neural Network in an energy and performance efficient way
Proposed solution
  Use DRAM error mask as device’s fingerprint to prevent being deployed on pirate devices
  We disable the DRAM read path and use a dynamic error mask selection scheme to protect error mask on client side
Results
  Neural Network can be effectively protected
  Achieve 72% and 44% improvement in performance and energy

## Slide 31
Thank you