## Slide 1: RACE-IT: A Reconfigurable Analog Computing Engine for In-Memory Transformer Acceleration
Lei Zhao, Aishwarya Natarajan, Luca Buonanno, Archit Gajjar, Ron Roth, Sergey Serebryakov, John Moon, Omar Eldash, Jim Ignowski, Giacomo Pedretti
Artificial Intelligence Research Lab (AIRL), Hewlett Packard Labs, USA

## Slide 2: Analog In-Memory Computing
Weight Buffer
PE
PE
PE
…
PE
PE
PE
…
PE
PE
PE
…
Input Buffer
…
…
…
Output Buffer
Memory
W
O
I
Memory
Input Buffer
Output Buffer
I
O
Digital Accelerator
Analog Dot-Product Engine (DPE)
Memory–compute separation → high data movement cost
Low energy efficiency
Reduced data movement → strong energy efficiency
Natural VMM via Ohm’s & Kirchhoff’s laws
Extremely high parallelism & compute density
Heavy DAC/ADC overhead (area & power)
Limited support for complex/nonlinear operations

## Slide 3: Challenges
Linear
Linear
Linear
DMMul_1
Scale
Softmax
DMMul_2
Linear
Linear
Linear
DMMul_1
Softmax
VFU
Linear
DMMul_2
Linear
Linear
Softmax
VFU
Linear
DMMul_1
VFU
DMMul_2
VFU
Self-Attention
DMMul: DPE
Softmax: VFU
DMMul: VFU
Softmax: VFU
= DPE
= DPE read
= DPE write
Non-VMM operations are pervasive in Attention
Data Dependent Matrix Multiplication (DMMul): both operands (e.g., Q, K) are dynamically generated for each input
  Opt 1: Frequent ReRAM reprogramming is required.
  Opt 2: Digital multipliers ( Vector Functional Units) are needed.
Softmax involves exponentiation and division operations.
New activations (e.g., GELU) may be introduced in future models.

## Slide 4: Challenges
Crossbar
Data movement
DAC
VFU
ADC
ISAAC
RAELLA
LeNet
ResNet18
SENet
EfficientNet
ResNet34
VGG11
ShuffleNet
DenseNet
BERT-tiny
MNIST
CIFAR10
ImageNet
GLUE
CNN
  Overhead mainly fromADCs converting analog DPE outputs to digital.
Attention
  ADC overhead remains.
  Energy is dominated by non-VMM ops (DMMul, Softmax, activation)

## Slide 5: Analog Content Addressable Memory (ACAM)
An ACAM cell has a 6T2M structure and can store an analog range (upper and lower thresholds).
The cell outputs a MATCH only if the input falls within its stored range.
In an ACAM array, multiple rows compare against the input vector in parallel.
A row outputs a MATCH only if all cells in that row match the input.
Computional principle
ACAM cell Structure
Computing with ACAM Array

## Slide 6: RACE: Reconfigurable Analog Computing Engine
RACE cell structure
Mode 1: Univariate 8-bit Comparison
8-bit input and thresholds
Decompose to 4-bit MSB and 4-bit LSB
MATCH: if input is in the range
Mode 2: Bivariate 4-bit Comparison
4-bit inputs and thresholds
2 inputs with their own ranges
MATCH: if both inputs are in their respective range
No hardware change for mode switch
Only depends on stored threshold and input value

## Slide 7: Activation (Univariate 8-bit Comparison Mode)
:
Dataset
RACE
Dataset
RACE
Each output bit is computed separately
Output Gray code reduces ~2X RACE array size

## Slide 8: DMMul (Bivariate 4-bit Comparison Mode)
z = x * y
3-bit input, 6-bit output
Each output bit is computed separately
Group 1s in a similar way as solving a Karnauph map
Each grouped rectangle is a range that will be stored in an ACAM cell

## Slide 9: DMMul (Bivariate 4-bit Comparison Mode)
Apply gray encoding changes the pattern, but the number of ranges does not necessarily change.
Apply more iterations of Gray encoding on top on the Gray-encoded output.
Find the best encoding depth with the least number of ranges.

## Slide 10: Decoding Gray Code
:
Gray code outputs have to be decoded to binary code before subsequent computations
Decoding only requires simple XOR gates
To support multi-depth decoding, the outputs of XOR gates are latched and fed back for additional decoding rounds
Decoding formula
Decoding Schematic

## Slide 11: Softmax
Exponentiation: implemented in RACE using Univariate 8-bit Comparison mode
Inversion: implemented in RACE using Univariate 8-bit Comparison mode
Multiplication: implemented in RACE using Bivariate 4-bit Comparison mode
Addition: performed by digital adders (well optimized, minimal overhead)

## Slide 12: Performance & Energy
453X performance speedup and 354X energy reduction over a H100 GPU.
15X speedup and 122x energy reduction over other IMC accelreators
Eyeriss: a PE array based digital accelerator
PUMA: a crossbar-based accelerator with VFU for non-VMM operations
ReTransformer: a crossbar-based accelerator that needs programming crossbars to compute DMMul

## Slide 13
Thank you